## Slide 1: National Ignition Facility Neutron Sources
Hardened Electronics and Radiation Technology
C.5
Charles B. Yeamans and Brent E. Blue
April 17, 2018

## Slide 2: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 3: National Ignition Facility Neutron Sources

## Slide 4: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 5: The National Ignition Facility is the world’s largest laser-driven neutron source.

## Slide 6: Overview: Using the NIF as a neutron source
Experiments enter through the NIF User Office or specific programs.
Based on user needs, individual experiments are fielded on an available NIF neutron yield shot.
Experiments are designed into a diagnostic instrument manipulator (DIM) or Target and Diagnostic Manipulator (TANDM), with design based on fluence an volume requirements.
 | Direct drive | Indirect drive
Capsule material | CH, SiO2 | CH, C, Be, other
Hohlraum material | n/a | Au, Au/DU
Fielding temperature | 293 K | 293 K, 18-120 K
DT yield | 4 x 1015 | 1.7 x 1016
Burn duration (ps) | 250 | 150-200
Neutron thermal temperature (keV) | 8-15 | 2-5
Maximum fluence available (n/cm2) |  | 
Destructive | 3 x 1014 | 3 x 1015
nondestructive | 6 x 1012 | 1.6 x 1013
DT neutrons per NIF optics log growth | 74 | 9

## Slide 7: Overview: Practical considerations for a NIF user
Experiments allocated through accepted program proposals (JNSAC/NSA, HED and ICF councils, Discovery Science) can select their experimental configuration to best use the allocation.
Ride-along: Any NIF DT yield shot (29 in FY17, 26 in FY16) may support additional experiments through coordination with the campaign experimental team. This includes NIF facility neutron calibration shots as well as programmatic.
Optics Use: NIF is a rare laser facility operating above the optics damage threshold. A computational laser performance model helps determine the “optics use” per proposed laser shot in units of damage log growth.
Shot cycle length: Allocation is usually made in “user days.” Neutron yield shots have lengthy neutron mitigation procedures. Typical planning is one yield shot per user day.
Debris and Shrapnel: The experimental planning process at NIF focuses on machine safety and maintaining experimental throughput.

## Slide 8: Overview: Fusion spectra available at NIF
All neutron sources have designs for 14 MeV deuterium-tritium (DT), 0-10 MeV pure tritium (TT), pure deuterium (DD), and He-3 and He-4 for charged particle sources.
Source yields for TT and DD are typically 1% of those for DT due to the difference in fusion reactivity of the respective species.
Energy spectrum per source neutron for different gas fills
Energy spectrum per source DT neutron for different burn temperatures

## Slide 9: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 10: NIF Neutron Sources: Direct Drive
Because the NIF beam geometry supports experiments with z-oriented hohlraums, experiments utilizing laser energy depositions directly on the imploding surface are configured in a pole-hot geometry.
Subsequent fundamental physics work has refined the PDD technique to produce reliable high neutron yields using a simple, low-mass target assembly.
The low-mass target assembly reduced the debris wind load substantially, allowing neutron experiments using PDD sources to reduce their source standoff.

## Slide 11: NIF Neutron Sources: Polar direct drive exploding pusher (PDXP)
Target
Material: CH (GDP)
Outer diameter: 2.9 mm
Thickness: 18 microns
Gas fill: 65:35 DT, 8 atm (1.6 mg/cc)
Temperature: warm (293 K)
PDXP Laser (28.6 % cone fraction)
~1015 W/cm2 at capsule
Neutron mode 1 (=0)
Neutron mode 2 (≠0)
As N_Sdev_ExPsh moves to improved capsules, x-ray yield is expected to increase 5x.
bang
drive
Time-resolved spatially-integrated x-ray emission
SPIDER: Shahab Khan
FNAD: Charles Yeamans
NTOF: SAVI dashboard
PDXP source is a pure 14 MeV DT fusion output from a nearly massless system.
Target downscatter is minimized and required experimental standoff is less than for cooled targets.
allows 5 cm source standoff
Targets are relatively easy to field, possible to execute 2 shots in one user shot/day.
 |  | PDXP
Inputs | Fill gas DT | 65:35
 | capsule pressure (torr) | 6080
 | Target temperature (K) | room
 | Laser energy (MJ) | 0.62
 | optics log growth per shot | 0.005
 | shot cycle time (h) | 9
Outputs | expected yield (DT) | 3.7 x 1015
 | Ťion (keV) | 12
 | burn width (ps) | 250-300
 | neutron volume (mm3) | 0.05
 | output spectrum | pure DT
 | minimum sample standoff (cm) | 1
 | minimum DLP standoff (cm) | 5
Metrics | 1015 neutrons/optics log growth | 740
 | doping capsule/fill | y/y
 | max fluence: destructive (n/cm2) | 2.9 x 1014
 | max fluence: non-destructive (n/cm2) | 1.2 x 1013

## Slide 12: NIF Neutron Sources: glass direct drive exploding pusher (DDEP)
diffusion-filled SiO2 capsule up to 2.1 mm in diameter
The diffusion filling process allows for precisely-tuned gas fills that may not be practically adapted to the NIF shot-time gas fill system
Max fuel pressure is limited only by capsule burst and not NIF gas delivery rating
ability to suppress DT yield using high-Z noble gas fill dopants.
2.1 mm
DT gas
SiO2
 |  | DDEP
Inputs | Fill gas DT | 50:50
 | capsule pressure (torr) | 7600
 | Target temperature (K) | room
 | Laser energy (MJ) | 0.82
 | optics log growth per shot | 0.01
 | shot cycle time (h) | 9
Outputs | expected yield (DT) | 8 x 1014
 | Ťion (keV) | 7
 | burn width (ps) | 250-300
 | neutron volume (mm3) | 0.05
 | output spectrum | pure DT
 | minimum sample standoff (cm) | 4
 | minimum DLP standoff (cm) | 5
Metrics | 1015 neutrons/optics log growth | 80
 | doping capsule/fill | n/y
 | max fluence: destructive (n/cm2) | 4.0 x 1012
 | max fluence: non-destructive (n/cm2) | 2.5 x 1012

## Slide 13: NIF Neutron Sources: Indirect Drive
indirect drive smooths the radiation profile impinging on the ablating surface substantially.
has been the choice of the NIF ICF ignition science program.
Indirect drive neutron sources have been developed and tested over a wide range of neutron yield and output spectrum parameters.
The target assemblies are relatively massive, therefore limiting the minimum source-experiment standoff.

## Slide 14: NIF Neutron Sources: indirect drive exploding pusher (IDEP)
By designing the capsule and laser around a minimum of ablator mass remining, a neutron source with negligible capsule or room return scatter can be created.
Because the target assembly relies on a hohlraum, experimenters have been successful using the hohlraum thermomechanical package as a mounting surface to conduct neutron experiments on small samples of materials, which are collected as debris postshot using standard nuclear forensic techniques.
 |  | IDEP
Inputs | Fill gas DT | 50:50
 | capsule pressure (torr) | 2487
 | Target temperature (K) | 32
 | Laser energy (MJ) | 0.71
 | optics log growth per shot | 0.027
 | shot cycle time (h) | 16
Outputs | expected yield (DT) | 5.5 x 1014
 | Ťion (keV) | 5
 | burn width (ps) | 250-300
 | neutron volume (mm3) | 0.05
 | output spectrum | pure DT
 | minimum sample standoff (cm) | 0.5
 | minimum DLP standoff (cm) | 10
Metrics | 1015 neutrons/optics log growth | 20
 | doping capsule/fill | y/y
 | max fluence: destructive (n/cm2) | 1.7 x 1014
 | max fluence: non-destructive (n/cm2) | 4.4 x 1011

## Slide 15: NIF Neutron Sources: DT gas-filled Symcap
cold capsule fill gas (32-128 K) allows fuel gas density up to 9 mg/cc
less complicated target operations and faster shot cycles than the layered platform.
HDC ablators may have DT yields up to 4.3 x 1015
GDP plastic ablators have yielded up to 8 x 1014, and may be doped with:
  a wide variety of materials through ion implantation or deposition during the capsule growth
  sub-microgram quantities of dopants for separated isotope cross section experiments
 |  | CH Sym | HDC Sym
Inputs | Fill gas DT | 50:50 | 50:50
 | capsule pressure (torr) | 2892 | 1478
 | Target temperature (K) | 32 | 32
 | Laser energy (MJ) | 0.91 | 1.3
 | optics log growth per shot | 0.025 | 0.11
 | shot cycle time (h) | 16 | 18
Outputs | expected yield (DT) | 8 x 1014 | 4.5 x 1015
 | Ťion (keV) | 2.8 | 3.8
 | burn width (ps) | 200-250 | 175-225
 | neutron volume (mm3) | 0.0009 | 0.0009
 | output spectrum | DT + 1% downscatter | DT + 0.5% downscatter
 | minimum sample standoff (cm) | 0.5 | 0.5
 | minimum DLP standoff (cm) | 10 | 10
Metrics | 1015 neutrons/optics log growth | 32 | 41
 | doping capsule/fill | y/y | n/y
 | max fluence: destructive (n/cm2) | 2.5 x 1014 | 1.4 x 1015
 | max fluence: non-destructive (n/cm2) | 6.3 x 1011 | 3.6 x 1012
20 nm DU layer
capsule inner surface
capsule outer surface
175 micron GDP
SymCDT target with mass-tamped hohlraum

## Slide 16: NIF Neutron Sources: DT cryogenic layered
Cryogenic DT ice layers are driven to convergence ratios of 20-35 to produce the highest NIF DT yields.
Capsules of different materials can be uses to select yield, spectrum properties, and dopant capability.
Experimental volume limited by shroud clearance.
High optics and facility time use: “expensive” shots.
 |  | layered
Inputs | Fill gas DT | 50:50
 | capsule pressure (torr) | 68
 | Target temperature (K) | 18.6
 | Laser energy (MJ) | 1.8
 | optics log growth per shot | 0.18
 | shot cycle time (h) | 24
Outputs | expected yield (DT) | 1.8 x 1016
 | Ťion (keV) | 3-5.5
 | burn width (ps) | 175-225
 | neutron volume (mm3) | 0.0001
 | output spectrum | DT + 1-5% downscatter
 | minimum sample standoff (cm) | 0.5
 | minimum DLP standoff (cm) | 10
Metrics | 1015 neutrons/optics log growth | 100
 | doping capsule/fill | y/n
 | max fluence: destructive (n/cm2) | 5.7 x 1015
 | max fluence: non-destructive (n/cm2) | 1.4 x 1013
A “shroud” is necessary to maintain temperature stability prior to shot. Clearance for shroud opening limits volume remaining for the neutron experiment.

## Slide 17: NIF Neutron Sources: Summary table
 |  | PDXP | DDEP | IDEP | CH Sym | HDC Sym | layered
Inputs | Fill gas DT | 65:35 | 50:50 | 50:50 | 50:50 | 50:50 | 50:50
 | capsule pressure (torr) | 6080 | 7600 | 2487 | 2892 | 1478 | 68
 | Target temperature (K) | room | room | 32 | 32 | 32 | 18.6
 | Laser energy (MJ) | 0.62 | 0.82 | 0.71 | 0.91 | 1.3 | 1.8
 | optics log growth per shot | 0.005 | 0.01 | 0.027 | 0.025 | 0.11 | 0.18
 | shot cycle time (h) | 9 | 9 | 16 | 16 | 18 | 24
Outputs | expected yield (DT) | 3.7 x 1015 | 8 x 1014 | 5.5 x 1014 | 8 x 1014 | 4.5 x 1015 | 1.8 x 1016
 | Ťion (keV) | 12 | 7 | 5 | 2.8 | 3.8 | 3-5.5
 | burn width (ps) | 250-300 | 250-300 | 250-300 | 200-250 | 175-225 | 175-225
 | neutron volume (mm3) | 0.05 | 0.05 | 0.05 | 0.0009 | 0.0009 | 0.0001
 | output spectrum | pure DT | pure DT | pure DT | DT + 1% downscatter | DT + 0.5% downscatter | DT + 1-5% downscatter
 | minimum sample standoff (cm) | 1 | 4 | 0.5 | 0.5 | 0.5 | 0.5
 | minimum DLP standoff (cm) | 5 | 5 | 10 | 10 | 10 | 10
Metrics | 1015 neutrons/optics log growth | 740 | 80 | 20 | 32 | 41 | 100
 | doping capsule/fill | y/y | n/y | y/y | y/y | n/y | y/n
 | max fluence: destructive (n/cm2) | 2.9 x 1014 | 4.0 x 1012 | 1.7 x 1014 | 2.5 x 1014 | 1.4 x 1015 | 5.7 x 1015
 | max fluence: non-destructive (n/cm2) | 1.2 x 1013 | 2.5 x 1012 | 4.4 x 1011 | 6.3 x 1011 | 3.6 x 1012 | 1.4 x 1013

## Slide 18: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 19: Many neutron experiments are assembled onto a single NIF shot.
 | capsule | hohlraum | support ring | DLP | Treefrog | HTOAD | SRC Toad | Snout-NAD | test well sample | reentrant well | port flange
distance from TCC (cm) | 0.1 | 0.5 | 1 | 5 | 7 | 45 | 50 | 50 | 350 | 375 | 550
sample area (cm2) |  | 0.05 | 3 | 90 | 0.5 | 20 | 4.9 | 20 | 37 | 1250 | 1250
sample depth (cm) |  | 0.05 | 0.5 | 20 | 0.14 | 8 | 0.1 | 1 | 1 | 1000 | 20
solid angle (msr) |  | 200 | 3000 | 3600 | 10 | 10 | 2.0 | 8.0 | 0.3 | 8.9 | 4.1
Volume (cm3) |  | 0.0025 | 1.5 | 1800 | 0.07 | 160 | 0.5 | 20 | 37 | 1.25 x 106 | 25,000
max DT neutron yield | 4.0 x 1014 | 1.7 x 1016 | 3.7 x 1015 | 3.7 x 1015 | 3.7 x 1015 | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016
max fluence (n/cm2) | 3.2 x 1015 | 5.4 x 1015 | 2.9 x 1015 | 1.2 x 1013 | 6.0 x 1012 | 6.7 x 1011 | 5.4 x 1011 | 5.4 x 1011 | 1.1 x 1010 | 1.1 x 1010 | 4.5 x 109

## Slide 20: NIF Neutron Experimental Platforms: exterior flange-mounted and reentrant well
A test well may be outfitted with a large-volume neutron experiment seeing up to 1010 n/cm2. Test volume is connected to target bay atmosphere.
Additional experiments may be positioned directly on exterior port flanges. (ex: “nuclear forensic signatures of common cellular telephones”)
Test well configuration for camera tests, with spatially-resolved neutron dosimetry.
 | test well sample | reentrant well | port flange
distance from TCC (cm) | 350 | 375 | 550
sample area (cm2) | 37 | 1250 | 1250
sample depth | 1 | 1000 | 20
solid angle (msr) | 0.3 | 8.9 | 4.1
volume | 37 | 1.25 x 106 | 25,000
max DT neutron yield | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016
max fluence (n/cm2) | 1.1 x 1010 | 1.1 x 1010 | 4.5 x 109

## Slide 21: NIF Neutron Experimental Platforms: Snout-mounted auxiliary experiments (passive)
8 cm depth
5 cm diameter
NIF diagnostic manipulators are used to carry ride-along experiments on neutron-yielding shots. This capability is readily accessible to collaborating groups.
Treefrog
1-2 g of HEU, DU, Th, Tm, Gd, Nd, Ir, Au, Fe
Pressurized gas cell
Neutron spectrum tailoring HTOAD
Target Option Activation Device (TOAD)
1000 torr
This is the experimental compliment to a MCNP design study in spectrum tailoring.
Collaboration with U.C. Berkeley Department of Nuclear Engineering
 | Treefrog | HTOAD | SRC Toad | Snout-NAD
distance from TCC (cm) | 7 | 45 | 50 | 50
sample area (cm2) | 0.5 | 20 | 4.9 | 20
sample depth | 0.14 | 8 | 0.1 | 1
solid angle (msr) | 10 | 10 | 2.0 | 8.0
volume | 0.07 | 160 | 0.5 | 20
max DT neutron yield | 3.7 x 1015 | 1.7 x 1016 | 1.7 x 1016 | 1.7 x 1016
max fluence (n/cm2) | 6.0 x 1012 | 6.7 x 1011 | 5.4 x 1011 | 5.4 x 1011

## Slide 22: NIF Neutron Experimental Platforms: User-designed dynamic load packages
Technicians install a National Security Applications ENP (Energetic Neutron Platform, Sandia Natl. Lab) in DIM 90-78 for a data collection shot awarded to the Sandia PI
(W. J. Martin) through the NIF User Office.
* Example based on Sandia TANDM ENP
Energy Tuning Assembly (ETA)
AFIT: Capt. James Bevins
UCB: Racheal Slaybaugh, Lee Bernstein, Bethany Goldblum
LLNL: William Dunlop, Dawn Shaughnessy, Charles Yeamans, Eugene Henry
The UCB/AFIT ETA is designed to transform a NIF neutron source into the objective TN+PFNS neutron spectrum.
2.6 m
17 cm
5.7 cm
The experimenter designs to fit within the available TANDM space.
 | DLP
distance from TCC (cm) | 5
sample area (cm2) | 90
sample depth | 20
solid angle (msr) | 3600
volume | 1800
max DT neutron yield | 3.7 x 1015
max fluence (n/cm2) | 1.2 x 1013
Energetic Neutron Platform (ENP)
SNL PI: William J. Martin

## Slide 23: NIF Neutron Experimental Platforms: Passive snout neutron spectrum tuning
110 cm
Al
Zr
In
Au
41 cm
7 cm
Al
Zr
In
Au
Al
Zr
In
Au
7.8 x 1012 n/cm2
1 MeV Si equiv.
1.6 x 1011 n/cm2
2.1 x 1010 n/cm2
A
A
ei wrt vacuum ideal transport
location | Standoff (cm) | isotope | N0/n/g measured | N0/n/g MCNP no density | N0/n/g MCNP sample only density | N0/n/g MCNP full density | design N0/n/g
kinematic base | 110 | Au196g | 3.20E-08 |  |  |  | 3.71E-08
kinematic base | 110 | Au198 | 1.61E-08 |  |  |  | 2.33E-11
kinematic base | 110 | In115m | 2.44E-09 |  |  |  | 1.87E-09
kinematic base | 110 | In116m | 1.88E-08 |  |  |  | 2.90E-11
kinematic base | 110 | Zr89 | 9.92E-09 |  |  |  | 1.14E-08
basket | 41 | Au196g | 2.10E-07 |  |  |  | 2.34E-07
basket | 41 | Au198 | 1.93E-08 |  |  |  | 1.47E-10
basket | 41 | In115m | 1.40E-08 |  |  |  | 1.19E-08
basket | 41 | In116m | 5.11E-08 |  |  |  | 1.85E-10
basket | 41 | Zr89 | 7.36E-08 |  |  |  | 7.33E-08
pinhole | 7 | Au196g | 9.81E-06 |  |  |  | 1.17E-05
pinhole | 7 | Au198 | 6.54E-08 |  |  |  | 7.34E-09
pinhole | 7 | In115m | 6.57E-07 |  |  |  | 6.30E-07
pinhole | 7 | In116m | 1.64E-07 |  |  |  | 9.77E-09
pinhole | 7 | Zr89 | 3.03E-06 |  |  |  | 3.45E-06

## Slide 24: NIF Neutron Experimental Platforms: hohlraum-mounted materials experiments
Solid collection efficiency is 8% of the total target mass in the line of sight to collector.
thulium
gadolinium
neodymium
NIF Nuclear cross sections: PI – Dawn Shaughnessy
Experimental group: Narek Gharibyan, Sherry Faye, John Despotopulos, Pat Grant, Ken Moody, Charles Yeamans
Primary objective: measuring 14 MeV neutron reaction cross sections relevant to post-detonation nuclear forensics
Results:
Debris emission from the target assembly is mostly outwardly radial as expected.
The added foil mass substantially changes the target disassembly dynamics.
Large Area Solid Radiochemistry collector (LASR)
NIF target fabrication: Brian Yoxall
Solid Radiochemistry Collector (SRC)

## Slide 25: NIF Neutron Experimental Platforms: high-Z dopant layer in the ablator
Capsule and hohlraum debris has been collected successfully on many shots.
NIF Nuclear Forensics: PI – Dawn Shaughnessy
Experimental group: Narek Gharibyan, John Despotopulos, Ken Moody, Pat Grant, Carol Velsko, Bill Cassata, Sherry Faye, Charles Yeamans, Ellen Edwards
Results:
Successful capsule debris collection. Completed experimental series using depleted uranium and conventional capsule fabrication. Development of experimental platform to study fission yield and neutron reaction cross sections under conditions relevant to the nuclear forensic program
Development of advanced doping techniques using micro/nanogram quantities of material.
 | Laser energy | DU recess | Fission yield1 | Collection efficiency2
N170130-003 | 0.9 MJ | 10 um | 6.56 | 1.53
N160210-001 | 0.9 MJ | 21 um | 4.54 | 0.07
N150907-003 | 1.3 MJ | 10 um | 8.70 | 0.12
DU hohlraum | 1.5 MJ | n/a | 1.00 | 1.00
Uranium-doped CH capsule
Mass-tamped hohlraum
20 nm DU layer
capsule inner surface
capsule outer surface
175 micron GDP
Photo: General Atomics
Photo: Sean Felker
NIF target fabrication
SymCDT target with mass-tamped hohlraum
CH plastic capsule, 175 micron thickness with 1016 atoms of depleted uranium.
Normalized 137,138,139Xe and 87,88Kr per 1015 neutrons
Normalized 97Zr (90-315) atoms/cm2 per 1015 neutrons
 | capsule | hohlraum
distance from TCC (cm) | 0.1 | 0.5
sample area (cm2) |  | 0.05
sample depth |  | 0.05
solid angle (msr) |  | 200
volume |  | 0.0025
max DT neutron yield | 4.0 x 1014 | 1.7 x 1016
max fluence (n/cm2) | 3.2 x 1015 | 5.4 x 1015

## Slide 26: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 27: Developmental Platforms: Capsule Microinjection Doping
Goal: Add 1016 radioactive atoms to the inner surface of a capsule
  More efficient and faster than sputtering or ion implantation; allows the use of radionuclides as dopant atoms
  Prevents issues related to outer surface roughness
Investigating direct surface coating with metal oxide aerogels (analogous to established foam doping methods)
Aerogel layer inside capsule (before drying)
Micro injector adding material through fill tube hole
John Despotopulos

## Slide 28: Neutron Source development: HYDRA calculates the combined environment target is a better source of both neutrons and x-rays than a bare capsule.
As a neutron source, a spherical metal foam shell on a capsule driven by a 2 ns square pulse is calculated to better than a bare capsule.
This combines two well-established target fabrication techniques.
Energy range (keV) | XRCE (%) |  | Foam/bare XRCE
 | with foam | bare capsule | 
0-1.5 | 9.5 | 7.5 | 1.3
1.5-3 | 3.9 | 2.7 | 1.4
3-7 | 9.2 | 0.95 | 9.7
7-10 | 0.27 | 0.09 | 3.0
10-250 | 0.93 | 0.05 | 18.6
0-250 | 24.4 | 11.6 | 2.1
2.9 mm GDP (Kelly Youngblood)
~12 mg/cc silver foam
(Sergei Kucheyev)
+
Addition of a metal foam layer, as is currently fabricated for x-ray source targets, is predicted to increase neutron yield 2-3x.

## Slide 29: Advanced Experimental Capability: Get the user experiments closer to the neutron source.
A support ring added to the target assembly decreases standoff substantially.
Experiments positioned on the ring see 14 MeV neutron fluences 100x greater than can be achieved at any other facility.
An articulated sample positioner would bring the nondestructive testing capability within the cryogenic shroud clearance to within 2 cm of a layered cryogenic neutron source.
 | support ring | support ring with improved source | articulated positioner
distance from TCC (cm) | 1 | 1 | 2
sample area (cm2) | 3 | 3 | 0.5
sample depth | 0.5 | 0.5 | 3
solid angle (msr) | 3000 | 3000 | 125
volume | 1.5 | 1.5 | 1.5
max DT neutron yield | 3.7 x 1015 | 1.3 x 1016 | 1.8 x 1016
max fluence (n/cm2) | 2.9 x 1015 | 1.0 x 1016 | 3.6 x 1014

## Slide 30: National Ignition Facility Neutron Sources outline
Abstract
NIF overview
  Using the NIF as a neutron source
  Practical consideration for the user
  Fusion spectra available
NIF neutron sources
  Polar direct drive
    CH PDXP
    SiO2 DDEP
  Indirect drive
    ICF cryogenic layered
    DT gas Symcaps
    IDEP
  Summary table
Experimental Platforms
  Exterior flange mounted and reentrant well
  Snout-mounted auxiliary positions
  Dynamic load packages
  Hohlraum
  Capsule
Neutron Source and Experimental Platform Development
  Capsule microinjection doping
  Neutron source development: yield enhancements
  Experimental support ring and reduced source standoff
Reference table

## Slide 31: NIF Neutron Sources: Reference Table
topic | reference
NIF facility | B M Van Wonterghem et al 2016 Fusion Sci. Technol. 69 452-469
NIF optics loop | K R Manes et al 2016 Fusion Sci. Technol. 69 146-249
NIF laser performance optimization module (optics use calculation) | M Shaw and R House, Proc SPIE, High Power Lasers for Fusion Research III; 93450E (2015)
NIF debris and shrapnel | N D Masters et al 2016 J. Phys.: Conf. Ser. 717 012108
NIF diagnostic instrument manipulators | R Plummer 2013 Proc. SPIE 8850 885005
NIF neutron spectra (DT) | B Appelbe and J Chittenden, High Energy Density Physics 11 (2014) 30-35
NIF neutron spectra (DT downscatter) | D C Wilson et al 2002 Nucl. Instrum. Meth. A 488 400–409
NIF neutron spectra (TT) | D T Sayre et al 2013 Phys. Rev. Lett. 111 052501
NIF neutron spectra (DD) | H Brysk 1973 Plasma Phys. 15 611
polar direct drive | N S Krasheninnikova, S M Finnegan, and M J Schmitt, Phys. Plasmas 19, 012702 (2012)
polar direct drive | R S Craxton et al., Physics of Plasmas 22, 110501 (2015)
Indirect drive Symcaps (experiment) | G A Kyrala et al., Physics of Plasmas 18, 056307 (2011)
Indirect drive Symcaps (simulation) | S V Weber et al., Physics of Plasmas 21, 112706 (2014)
indirect drive layered sources | N B Meezan et al 2017 Plasma Phys. Control. Fusion 59 014021
indirect drive layered sources, HDC | S Le Pape et al “Energy gain from an imploding shell at the National Ignition Facility,” submitted to Physical Review Letters
indirect drive target engineering | A V Hamza et al. 2016 Fusion Sci. Technol. 69 395-406
indirect drive target engineering | T Parham et al 2016 Fusion Sci. Technol. 69 407-419
indirect drive exploding pushers | S Le Pape et al. Phys. Rev. Lett. 112 225002 (2014)
IDEPs for nuclear forensics | D A Shaughnessy et al 2016 J. Phys.: Conf. Ser. 717 012080
NIF solid debris collection capability | D A Shaughnessy et al 2012 Rev. Sci. Instrum. 83 10D917
enhanced NIF solid debris collection capability | C Waltz et al 2017 Proc. SPIE 10390 103900H
NIF HEU fission yield measurements | N Gharibyan et al. 2015 J. Radioanal. Nucl. Chem. 303 1335
NIF passive neutron experiments | C B Yeamans and N Gharibyan 2016 Rev. Sci. Instrum. 87 11D702
gas cell capability at NIF | A Ratkiewicz et al 2016 Rev. Sci. Instrum. 87 11D825
neutron effects measurements at NIF | W J Martin et al 2017 Journal of Radiation Effects, Research and Engineering 35
neutron effects measurements at NIF | W J Martin, submitted to Journal of Radiation Effects, Research and Engineering