## Slide 1
Application of Spectral Shaping for Simulating Neutron Environments
Lt Nick Quartemont
MS Nuclear Engineering 19M
Air Force Institute of Technology
21 July 2018

## Slide 2: Overview
Motivation
Research Objectives
Nuclear Data Covariance
Energy Tuning Assembly Design
Energy Tuning Assembly Analysis
Summary

## Slide 3: Motivation
Create spectrally accurate neutron energy flux environment
  Nuclear weapons effects
  Forensics exercises
2018 Nuclear Posture Review key efforts in countering nuclear terrorism - “deterring state support for nuclear terrorism through advanced forensics and attribution capabilities.”

## Slide 4: Research Objectives
Energy tuning assembly (ETA) optimized for synthetic weapons debris production
  ETA 1 – 2019 proof of concept experiment at National Ignition Facility (NIF)
  ETA 2 – Proposed 2020 shot at NIF
Explore ETA for ‘short pulse’ neutron source
  Proposed for 2020 shot at NIF

## Slide 5: ETA Research Objectives
Research Question:
Can we produce an accurate fission product distribution expected from a "typical" thermonuclear or boosted nuclear weapon detonation using spectral modification at the NIF?

## Slide 6: ETA2 Research Objectives
Enhanced efficiency for generating synthetic fission debris
Investigate capability for use as a short pulse neutron source
Increase number of fissions to ~
Define more realistic neutron spectrum
Updated NIF constraints
Run Coeus
Time profile of neutron flux
Energy spectrum of incident neutron flux
Run Coeus

## Slide 7: ETA Analysis
Coeus v1.0
Problem Constraints
Problem Objectives
Energy Tuning Assembly Design
SCALE 6.2
252 Energy Group Covariance Analysis
MCNP 6.1 and 5.1
Continuous Energy Transport Analysis
Radiation
Transport
Additional
Analysis
Optimize Foil Diagnostic Activation Pack
GEF
Fission Product Isotopes
STAYSL
Neutron Energy Spectra Unfold

## Slide 8: SCALE Nuclear Data Covariance Libraries
Distributed with 252 and 56 energy group structure
Based on evaluated covariance data and approximate data
  ENDF/B-VI,VII.1,VII.2-previously proposed
  JENDL-4.0
  Collaborative research with Brookhaven National Laboratory, Los Alamos National Laboratory, and Oak Ridge National Laboratory
  Working Party on International Nuclear Data Evaluation Co-operation (WPEC) Subgroup-26
SCALE has corrected correlation data to meet the definition of a correlation matrix (ie. Maximum value of 1)

## Slide 9: SCALE Nuclear Data Covariance
Evaluated nuclear data comes in as a correlation matrix, which can create a covariance matrix with the uncertainty
U-235 (n,f) Bi-209 (n,2n)
U-235 relative uncertainty peaks near 2.23 keV at 133.6%

## Slide 10: Energy Tuning Assembly Design
NIF Source 15 cm from cone base
~28 cm
~28 cm
Notes: ETA created with the Coeus v1.0 metaheuristic optimization software package
Objective thermonuclear and prompt fission neutron spectrum (TN+PFNS).
Input spectrum NIF D-T fusion
Optimize flux in highly enriched uranium (HEU) foil adjacent to Target Option Activation Device (TOAD)
Base of cone originally 6 cm from neutron source (moved to 15 cm)

## Slide 11: NIF Neutron Source
Appelbe HiFoot Time of Flight
Notes: 14.1 MeV in 250-300 ps
Nominal yield of 3.7E+15 neutrons
Source deviates from theoretical from “room return” and downscatter including fusion compression techniques

## Slide 12: NIF Neutron Source
DT Fusion
Zero
Temperature
Source
Notes: 14.1 MeV in 250-300 ps
Nominal yield of 3.7E+15 neutrons
Source deviates from theoretical from “room return” and downscatter including fusion compression techniques

## Slide 13: SCALE MAVRIC Sequence
Notes: 10.75 keV temperature plasma fusion source
Point source 15 cm from cone base of ETA

## Slide 14: ETA HEU Foil Incident Neutron Energy Spectrum

## Slide 15: 59 Group HEU Foil Incident Neutron Energy Spectrum

## Slide 16: HEU Foil Fissions

## Slide 17: Source Impacts on Reactions

## Slide 18: In-115 (n,g) Example Case
***16 SAMPLER Cases, results not converged
Output from SAMPLER

## Slide 19: Results
Modeled ETA with covariance is consistent with the continuous energy solution
Covariance adds about 1% relative uncertainty for well studied reactions (ex. U-235) and adds above 10% for less well studied reactions (ex. U-234)
Future work to add to this research:
  Increased number of samples until mean and relative error have converged.
  Move to real NIF spectrum

## Slide 20: Summary
Motivation
Research Objectives
Nuclear Data Covariance
Energy Tuning Assembly Design
Energy Tuning Assembly Analysis
Summary

## Slide 21: Questions

## Slide 22: Backups

## Slide 23: Covariance (What is it?)
Covariance is a measure of the linear relationship between two variables.
Alternative form of error propagation formula in Leo’s Techniques for Nuclear and Particle Physics Experiments
Not including covariance may introduce errors
Can normally be omitted in counting experiments

## Slide 24: ENDF/B-VII.1 vs SCALE 252 Group Correlation Matrix
ENDF/B-VII.1 SCALE 6.2 252 Group

## Slide 25: U-235 (n,f) 252 Group Structure

## Slide 26: Combining Responses from Perturbed Nuclear Data
Unperturbed
Response
N Sampled Responses with Perturbed Nuclear Data
Combine Data with Bootstrapping
Final Response with Statistical and Nuclear Data Covariance Uncertainty
SCALE Sampler Module
Sampled with replacement from each Sampler case and Gaussian distribution based on response statistical uncertainty

## Slide 27: NIF Neutron Source
Surface Source Read file from LLNL
Contains NIF “room return”, which accounts for less than 1% of source.

## Slide 28: Fission Product Isotopes
ENDF uses thermal, watt fission spectrum, and fast neutron spectra to provide fission product yields.
Determining fission product yields a priori can have relative errors on the order of 10%.
Options:
  Fit experimental data to phenomenological model.
  Use A General Description of Fission Observables (GEF)

## Slide 29: Unfolding the Neutron Spectrum From Foil Activation
If statistical and measurement error were zero, the activity could be extracted directly into a group structure.
The irradiation occurs on the order of a nanosecond, so the activation can be simplified without decay:
Error is always present, so a least squares approach is needed
PNNL’s STAYSL for radiation dosimetry has this capability

## Slide 30: Foil Diagnostic Activation Pack

## Slide 31: Foil Diagnostic Activation Pack
Notes: Activities are on the order of what is needed for counting experiments
Foils can be counted in a High Purity Germanium Detector (HPGe)
Large increase in uncertainty based on reaction data uncertainty.