## Slide 1
NUCLEAR DATA COVARIANCE ANALYSIS OF AN ENERGY TUNING ASSEMBLY FOR SIMULATING NUCLEAR WEAPON ENVIRONMENTS
Capt Nick Quartemont
MS Nuclear Engineering 19M
Air Force Institute of Technology
31 January 2019

## Slide 2: Motivation
2018 Nuclear Posture Review “deterring state support for nuclear terrorism through advanced forensics and attribution capabilities.”
Create accurate surrogate nuclear weapon neutron environment
Addresses deterrence and non-proliferation capability gaps:
  Attribution
  Certification and testing
Notes: The 2018 U.S. National Defense Strategy identied the modernization of the nu-
clear triad as a key capability to meet requirements [3]. Therefore, there is still a need
for the capabilities previously provided through nuclear testing for the study of nu-
clear environments to support the credibility of the nuclear deterrent. Previous work
has shown that the loss of nuclear testing has created a capability gap to reproduce
nuclear weapon environments of interest to national security applications including
nuclear weapons effects (NWE) and technical nuclear forensics (TNF).

## Slide 3: Problem: Capability gap in reproducing nuclear weapon environments
Notes: A key consideration for testing is the neutron energy spectrum in comparison with the environment that a nuclear weapon would see or produce.
A particular spectrum of interest is the combination of a thermonuclear (TN) and prompt fission neutron spectrum (PFNS) as the present testing does not address this region to a large extent.
The vast majority of testing facilities are focused on the Watt-fission spectrum, while a few are capable of producing the 14.1 MeV TN component from the deuterium-tritium (DT) fusion process\cite{Bridgman}.
The current prompt neutron facilities available are not well suited for the TN+PFNS application testing because of the lack of high energy neutrons, or there is not a large enough flux of neutrons on target.
Several examples of testing facilities for prompt neutrons outlined in Table \ref{tab:NWECap} are the Sandia Pulsed Reactor III (SPR), Sandia Annual Core Research Reactor (ACCR), White Sands Missile Range (WSMR) Fast Burst Reactor (FBR), and the Los Alamos National Laboratory (LANL) Rotating Target Neutron Source (RTNS).
The differential spectral profile of these sources compared to a notional TN+PFNS is shown in Figure \ref{fig:CompSource}. the LANL Weapons Neutron Research facility (WNR).

## Slide 4: Solution: Energy Tuning Assembly (ETA)
ETA Sample Cavity
HEU
Au, Zr, Ni, Al, In, W, Mn
NIF SOURCE
15 cm

## Slide 5: Experimental Overview and Full NIF Model
NIF Neutron Source with Mounted ETA Incident Laser Exclusion Zone
Modeled Polar Drive Exploding Pusher (PDXP) Deuterium-Tritium neutron source
3.7 x 1015 14 MeV neutron yield
Minimal downscatter compared indirect drive methods utilizing a hohlraum
Notes: including the target positioner (TARPOS), Target and Diagnostic Manipulator (TANDM) with ETA and diagnostic snout, polar diagnostic instrument manipulator (DIM), and target chamber with first panel walls

## Slide 6: Methodology

## Slide 7: ETA Neutron Energy Distribution Performance
Below 52 keV 1.2% total fluence
Pearson r
H0 : no correlation between the datasets
Reject if p-value > 0.05
Kolmogorov-Smirnov (KS) – 2 Sample
H0 : drawn from the same distribution
Reject if p-value < 0.05

## Slide 8: GEF Fission Product Mass Chain Distribution Results
Modeled ETA produced fission products are consistent to predicted TN+PFNS within error.
ETA Produced fissions
ETA – TN+PFNS Residuals

## Slide 9: STAYSL Unfolded Spectrum
182 Sampled Activation Results
81.9% of samples were not-rejected with a p-value greater than 0.05
18.1% of samples were rejected with a p-value lower than 0.05
  H0 : Two sets of data are governed by the same expected distribution

## Slide 10: Conclusions
Provide experimental data to further enable post-detonation attribution through enhanced technical nuclear forensics
  Representative neutron environment
  Modeled ETA fission products consistent with TN+PFNS
  fissions (order of ground sample collection)
Moderate impact of nuclear data covariance
  ~ 1% for integral reactions with low uncertainty (Fluence, (n,f))
  ~3-20% for activation foil reactions
Strong probability (80%) of unfolding successfully without iterating
Enhanced confidence for Q4 2019 NIF experiment

## Slide 11: Questions?