## Slide 1
Application of Spectral Shaping for Simulating Nuclear Relevant Neutron Environments
Lt Nick Quartemont
MS Nuclear Engineering 19M
Air Force Institute of Technology
29 May 2018

## Slide 2: Overview
Motivation
Research Objectives
Nuclear Data Covariance
Energy Tuning Assembly Design
Energy Tuning Assembly Analysis
  Neutron Energy Spectrum
  Fission Products
  Foil Diagnostic Activation Pack
  Unfolding Incident Neutron Spectrum
Summary

## Slide 3: Motivation
Create spectrally accurate neutron energy flux environment
  Nuclear weapons effects
  Forensics exercises
2018 Nuclear Posture Review key efforts in countering nuclear terrorism - “deterring state support for nuclear terrorism through advanced forensics and attribution capabilities.”

## Slide 4: Research Objectives
Energy tuning assembly (ETA) optimized for synthetic weapons debris production
  ETA 1 – 2019 proof of concept experiment at National Ignition Facility (NIF)
  ETA 2 – Proposed 2020 shot at NIF
Explore ETA for ‘short pulse’ neutron source
  Proposed for 2020 shot at NIF

## Slide 5: ETA Research Objectives
Research Question:
  Can we produce an accurate fission product distribution expected from a "typical" thermonuclear or boosted nuclear weapon detonation using spectral modification at the NIF?
Main ETA Analysis Areas:
  Refine list of fission products for radiochemical analysis
  Design foil activation diagnostic pack
  Simulated results including nuclear data covariance for neutron energy spectrum, foil activation rates, and fission product production rates

## Slide 6: ETA2 Research Objectives
Enhanced efficiency for generating synthetic fission debris
Investigate capability for use as a short pulse neutron source
Increase number of fissions to ~
Define more realistic neutron spectrum
Updated NIF constraints
Run Coeus
Time profile of neutron flux
Energy spectrum of incident neutron flux
Run Coeus

## Slide 7: ETA Analysis
Coeus v1.0
Problem Constraints
Problem Objectives
Energy Tuning Assembly Design
SCALE 6.2
252 Energy Group Covariance Analysis
MCNP 6.1 and 5.1
Continuous Energy Transport Analysis
Radiation
Transport
Additional
Analysis
Optimize Foil Diagnostic Activation Pack
GEF
Fission Product Isotopes
STAYSL
Neutron Energy Spectra Unfold

## Slide 8: SCALE Nuclear Data Covariance Libraries
Distributed with 252 and 56 energy group structure
Based on evaluated covariance data and approximate data
  ENDF/B-VI,VII.1,VII.2-previously proposed
  JENDL-4.0
  Collaborative research with Brookhaven National Laboratory, Los Alamos National Laboratory, and Oak Ridge National Laboratory
  Working Party on International Nuclear Data Evaluation Co-operation (WPEC) Subgroup-26
SCALE has corrected correlation data to meet the definition of a correlation matrix (ie. Maximum value of 1)

## Slide 9: U-235 (n,f) 252 Group Structure

## Slide 10: Covariance (What is it?)
Covariance is a measure of the linear relationship between two variables.
Alternative form of error propagation formula in Leo’s Techniques for Nuclear and Particle Physics Experiments
Not including covariance may introduce errors
Can normally be omitted in counting experiments

## Slide 11: ENDF/B-VII.1 vs SCALE 252 Group Correlation Matrix
ENDF/B-VII.1 SCALE 6.2 252 Group

## Slide 12: SCALE Nuclear Data Covariance
Evaluated nuclear data comes in as a correlation matrix, which can create a covariance matrix with the uncertainty
Cross-sections: U-235 (n,f) Bi-209 (n,2n)
U-235 relative uncertainty peaks near 2.23 keV at 133.6%

## Slide 13: Combining Responses from Perturbed Nuclear Data
Unperturbed
Response
N Sampled Responses with Perturbed Nuclear Data
Combine Data with Bootstrapping
Final Response with Statistical and Nuclear Data Covariance Uncertainty
SCALE Sampler Module
Sampled with replacement from each Sampler case and Gaussian distribution based on response statistical uncertainty

## Slide 14: Energy Tuning Assembly Design
ETA created with the Coeus v1.0 metaheuristic optimization software package
Objective thermonuclear and prompt fission neutron spectrum (TN+PFNS).
Input spectrum NIF D-T fusion
Optimize flux in highly enriched uranium (HEU) foil adjacent to Target Option Activation Device (TOAD)
Base of cone originally 6 cm from neutron source (moved to 15 cm)

## Slide 15: NIF Neutron Source
14.1 MeV in 250-300 ps
Nominal yield of 3.7E+15 neutrons
Source deviates from theoretical from downscatter including fusion compression techniques

## Slide 16: NIF Neutron Source
Surface Source Read file from LLNL
Contains NIF “room return”, which accounts for less than 1% of source.

## Slide 17: SCALE MAVRIC Sequence
10.75 keV temperature plasma fusion source
Point source 15 cm from cone base of ETA
Still in process of validating model and comparing SCALE results to MCNP
Adjoint Flux neutrons on HEU foil

## Slide 18: ETA HEU Foil Incident Neutron Energy Spectrum

## Slide 19: ETA HEU Foil Incident Neutron Energy Spectrum

## Slide 20: HEU Foil Fissions

## Slide 21: Foil Diagnostic Activation Pack
Notes: Activities are on the order of what is needed for counting experiments
Foils can be counted in a High Purity Germanium Detector (HPGe)
Large increase in uncertainty based on reaction data uncertainty.

## Slide 22: Fission Product Isotopes
ENDF uses thermal, watt fission spectrum, and fast neutron spectra to provide fission product yields.
Determining fission product yields a priori can have relative errors on the order of 10%.
Options:
  Fit experimental data to phenomenological model.
  Use A General Description of Fission Observables (GEF)

## Slide 23: Unfolding the Neutron Spectrum From Foil Activation
If statistical and measurement error were zero, the activity could be extracted directly into a group structure.
The irradiation occurs on the order of a nanosecond, so the activation can be simplified without decay:
Error is always present, so a least squares approach is needed
PNNL’s STAYSL for radiation dosimetry has this capability

## Slide 24: Summary
Motivation
Research Objectives
Nuclear Data Covariance
Energy Tuning Assembly Design
Energy Tuning Assembly Analysis
  Neutron Energy Spectrum
  Fission Products
  Foil Diagnostic Activation Pack
  Unfolding Incident Neutron Spectrum
Summary

## Slide 25: Questions

## Slide 26: Backups

## Slide 27: Foil Diagnostic Activation Pack